## Slide 1: Magnetic Control of Liquid Mirrors in Microgravity
DARPA Zenith Lecture 1
August 25
Álvaro Romero-Calvo, Ph.D.

## Slide 2: Liquid Mirror Telescopes (LMT)
A historical overview

## Slide 3
Newton’s Philosophiae,
Book 1: Definitions – Scholium,
1687

## Slide 4: First attempt, 1909
R.W. Wood, “The Mercury Paraboloid as a Reflecting Telescope”, Astrophysical Journal, Vol. 29, p. 164, 1909

## Slide 5: Modern LMTs, 1982-1989
Ermann F. Borra, The Liquid Mirror Telescope as a Viable Astronomical Tool, J. Roy, Astron. Soc. Can, Vol. 76, No. 4, 1982

## Slide 6: First astronomical use of an LMT, 1989

## Slide 7: The Large Zenith Telescope

## Slide 8: The 4m International LMT

## Slide 9: Analytical approach to low-gravity liquid interfaces
“The only rules that really matter are these:
What a man can do and what a man can't do”
Jack Sparrow

## Slide 10: State of the art for microgravity mirrors
There is one question that may have been overlooked:
Previously proposed solutions: high-viscosity liquid cycling, thermal fields, Lorentz forces, spherical mirrors, active correction, ferrofluids…
Unfortunately, previous works on ferrofluid-based liquid mirrors…
  Introduce non-scalable magnetic configurations in terms of geometry, power, or propellant management (e.g. continuous thrust)
  Employ questionable fluid and electromagnetic models: no fluid-magnetic coupling, completely ignore surface tension, do not consider important disturbance factors, do not set a clear target/application, etc.
Large-radius ground telescopes are limited by self-induced winds
Is it feasible to produce the surface profile we need in microgravity?

## Slide 11: The axisymmetric meniscus
Equilibrium liquid-gas interface (meniscus)
Mass-force potential
Microgravity
Solution:
No rotation (): Constant curvature (sphere)  Valid for spherical mirrors
Rotation ():
Axisymmetric liquid interfaces naturally adopt spherical profiles in microgravity
We need additional body forces to generate paraboloid surfaces

## Slide 12: Using ferrofluids
An alternative that may solve the problem in 3 steps

## Slide 13: Step 1: Generating a suitable force field
“Standard” magnet
Uniform magnetization
Analogous to what has already been proposed
Inhomogeneous field
Force “concentrated” in extremes
Halbach Array
Oriented magnetization vectors
Quasi-uniform force on one axis
Can be simplified to alternate polarity (simpler config., lower performance)
Scalable
Readily available (N52 magnets)
Tunable, with some work

## Slide 14: Step 1: Generating a suitable force field
Magnetic forces in Halbach array
Very significant ()
Homogeneous decay in …
…of the form
Disturbances in :
  Almost negligible
  1 order of magnitude smaller that
  Can be reduced by design (e.g. using smaller magnets)
Halbach arrays provide a means to homogenize the magnetic force potential distribution on ferrofluids

## Slide 15: Step 1: Generating a suitable force field
Zhang et al., “Analysis and comparison of two two-dimensional Halbach permanent magnet arrays for magnetically levitated planar motor”, Journal of Applied Physics 115, 17E704, 2014
… and all of this applies to 2D problems as well

## Slide 16: Step 2: Exploiting the force field
Strategy 1: Artificially-induced gravity using Halbach arrays + rotation
Equilibrium liquid-gas interface (meniscus)
Mass-force potential (including magnetic terms)
Non-capillary
Capillary
Only feasible for small deformations
(i.e. large focal lengths!)

## Slide 17: Step 2: Exploiting the force field
Strategy 2: Equipotential tuned surface using Halbach arrays. No rotation
Debris
Shield
Ferrofluid layer
Also works for
1 g tilting!!

## Slide 18: Force field of tilted Halbach magnet array

## Slide 19: Step 3: Finding a suitable ferrofluid
Task 1:
  Characterize optical properties of existing Vacuum Seal Grade (VSG) ferrofluids
  Test outgassing in application context
  Define operational T range (usually < 70º-100º C)
Task 2:
  Explore optically enhanced ferrofluids (e.g. metal-based, metal liquid-like films, etc.)
  Characterize optical properties

## Slide 20: Questions?
DARPA Zenith Lecture 1